## Slide 1
DFM Inspector
Automated Design for Manufacturability Analysis
Catch DFM violations before parts hit the shop floor
Capabilities Overview

## Slide 2
What is DFM Inspector?
A web and CLI tool that analyzes 3D CAD models for manufacturability.
• Loads native CAD geometry (STEP, IGES, STL) and inspects topology directly
• Applies industry-standard DFM rules across multiple manufacturing processes
• Uses ray-casting (used in computer graphics) for accurate measurements rather than bounding-box estimates
• Generates color-coded HTML, JSON, and Word reports with 3D renderings
• Highlights violations with severity, location, and recommended fixes

## Slide 3
Capabilities at a Glance
Multi-Format CAD
STEP / .stp
IGES / .igs
STL meshes
Auto unit detection
General DFM Checks
Wall thickness
Draft angles
Undercuts
Corner radii
Ribs and bosses
Tolerances
Welding DFM
AWS D1.1 / D1.2
AWS D1.3 / D1.6
Groove and skewed joints
Filler material recs
Process-Specific
CNC machining
Sheet metal
Injection molding
Process-tuned thresholds
Feature Detection
Holes (dia, depth)
Bends (angle, radius)
Pockets and corners
Spatial proximity
Reporting and Visuals
HTML interactive
JSON for tooling
Word with 3D renders
Severity color coding

## Slide 4
The Engine Under the Hood
Design Guidelines Documents
930-00163_R01 DESIGN GUIDELINE, INTEGRAL SKIN PU FOAM MOLDING
930-00164_R01 DESIGN GUIDELINE, THERMOPLASTIC INJECTION MOLDING
930-00166_R01 DESIGN GUIDELINE, HIGH PRESSURE DIE CAST AND GRAVITY CAST PERMANENT MOLD
930-00172_R01 DESIGN GUIDELINE, SHEET METAL
960-0075_R11 ENGINEERING DRAWING STANDARDS
960-0075-01_R03 ENGINEERING DRAWING STANDARDS, SOLIDWORKS TEMPLATE LAYERS
960-00169_R01 DESIGN GUIDELINE, WELDMENTS
960-00207_r02 AMAZON ROBOTICS WELDING REQUIREMENTS
Amazon Sheet Metal DFM Requirements for Verification
CNC_Machining_DFM_Guidelines
Injection Molding Process next level & Mold Val. Eng. Tech. Rev
MachinerysHandbkOBERG
Roll_Forming_Tolerances
Injection Molding Qualifications

## Slide 5
Supported CAD Formats
Native B-Rep parsing for accurate geometry analysis
STEP (.step / .stp)
Industry-standard CAD exchange format. Full B-Rep topology preserved, ideal for machining and assemblies.
IGES (.iges / .igs)
Legacy CAD exchange format still common from older systems. Surface and solid geometry supported.
STL (.stl)
Mesh format for 3D printing and quick visualization. Faster loading, lower geometric fidelity.

## Slide 6
General DFM Checks
Standard manufacturing rules applied automatically
Check | What it catches | Why it matters
Wall thickness | Too thin / too thick / non-uniform walls | Prevents warping, sink marks, blow-out
Draft angles | Insufficient draft for mold release | Enables clean part ejection
Undercuts | Geometry that traps the part in the mold | Avoids costly side actions
Corner radius | Sharp internal corners | Reduces stress concentration, tool wear
Ribs and bosses | Disproportioned reinforcement features | Prevents sink and short-shots
Tolerances | Unrealistically tight tolerances | Controls manufacturing cost

## Slide 7
From Kiro to AgentSpace
Five-stage pipeline: code generation to team release
1
Generate
Kiro
AI generates Python app from spec (requirements -> design -> tasks)
Hours
2
Run Local
Localhost
pip install + python app.py -> Flask on port 5000
Hours
3
Back Up
code.amazon.com
VPN + mwinit, push to feature branch (never mainline)
~1 hour
4
Review & Merge
CRUX (cr CLI)
Cloud Desktop runs cr to merge into mainline
~1 day
5
Release
AgentSpace
Upload rules MD, generate HTML dashboard, share URL
~1 hour
Minimum viable path: stages 1, 2, and 5 in a single day. Stages 3 and 4 are required only when the live app needs pipeline-based deployment.

## Slide 8
What Happens at Each Stage
Key actions, decisions, and gotchas
1. Generate
Spec-driven code gen
requirements -> design -> tasks -> code
Output
Flask app with CadQuery / OpenCascade geometry analysis
2. Run Local
Stack
Python 3.11+, Flask on localhost:5000
Verify
Upload STEP file, confirm DFM analysis runs
Gotcha
Disconnect Zscaler/VPN when testing localhost
3. Back Up
Auth
Cisco VPN + mwinit -f (~20h SSH cert)
Push
git push origin HEAD:refs/heads/initial-import
Gotcha
Never push to mainline; avoid folder/file name collisions on Windows
4. Review & Merge
Tool
cr CLI (Linux only)
Options
Cloud Desktop, teammate with one, or WSL
Gotcha
Defer this stage if you only need an AgentSpace release
5. Release
Path A (fast)
Upload rules MD + PDFs, generate HTML, share URL
Path B (live app)
Local install -> Cloud Desktop -> Pipeline + Apollo

## Slide 9
Welding DFM (AWS Compliance)
Material-specific rules for welded assemblies
AWS Standards Supported
AWS D1.1 / D1.1M
Structural Welding Code - Steel
AWS D1.2 / D1.2M
Structural Welding Code - Aluminum
AWS D1.3 / D1.3M
Structural Welding Code - Sheet Steel
AWS D1.6 / D1.6M
Structural Welding Code - Stainless Steel
AWS A2.4
Standard Symbols for Welding
Inspection Coverage
• Groove angles (50-65 degrees depending on material)
• Skewed joint beveling requirements based on joint angle
• Weld access (gun clearance and arc visibility)
• Material thickness minimums per AWS D1.x
• Root opening sizing for full penetration
• CJP vs PJP joint design and fillet weld sizing
• Filler material recommendations per parent material

## Slide 10
Process-Specific Rules
Different process, different thresholds
CNC Machining
• Wall >= 0.8mm aluminum, 1.0mm steel
• Hole depth-to-diameter <= 4:1 (10:1 deep)
• Internal corner >= 1/3 depth or 0.5mm
• Envelope <= 500x500x500 mm
• Feature size >= 2.0mm for standard tooling
Sheet Metal
• Bend radius >= 1.0mm aluminum, 1.5mm steel
• Hole-to-edge distance >= 2.0mm
• Wall >= 0.5mm aluminum, 0.8mm steel
• Hole-to-bend proximity check
• Hole-to-hole spacing per design guideline
Injection Molding
• Wall thickness 0.8 to 4.0 mm
• Draft >= 1 degree minimum
• Corner radii >= 0.5mm
• Uniform wall variation
• Boss and rib proportions

## Slide 11
Geometric Feature Detection
B-Rep topology analysis via CadQuery / OpenCascade
Holes
Diameter, depth, axis, location. Auto-classified as through, blind, counterbore, countersink.
Corners
Internal radii, angles, type (internal/external). Flagged when below process minimum.
Pockets
Dimensions, corner radii, depth-to-width. Validated against tooling reach.
Bends (sheet metal)
Bend axis, angle, radius. Used for hole-to-bend proximity.
Planar faces
Normal, area. Used for wall thickness and draft analysis.
Spatial relationships
Hole-to-hole, hole-to-edge, hole-to-bend distances.

## Slide 12
Measurement Accuracy
Ray-casting vs bounding-box estimation
Before (bounding-box)
• Estimated wall thickness from envelope
• Tolerance: +/- 10 to 20 mm
• False errors on thin-wall parts
• No location data on violations
• No feature classification
Now (ray-casting + B-Rep)
• Ray-cast wall thickness on real geometry
• Tolerance: +/- 0.01 mm
• Exact 3D coordinates per violation
• Auto-classified holes, corners, pockets
• Process-specific severity grading

## Slide 13
3D Visualization and Reports
Output Formats
HTML
Interactive report with severity color coding, expandable findings, embedded 3D views.
JSON
Machine-readable, versioned schema for integration with PLM and review tools.
Word (.docx)
Formatted document with multi-view 3D renderings and per-violation tables.
Severity coding: Red = critical | Orange = warning | Yellow = optimization

## Slide 14
Architecture
Flask web app + Python API
Web UI (Flask)
Drag-and-drop upload, run analysis, browse violations, export report
CAD Parser
STEP/IGES via pythonocc-core (OCP), STL via trimesh
Feature Extractor
CadQuery + OpenCascade B-Rep traversal
DFM Inspector Engine
Process-specific rule evaluation, severity grading
Rule Config
YAML-driven thresholds, easy to customize per program
Reporters
HTML / JSON / Word generation with 3D rendering hooks

## Slide 15
Industry Standards Referenced
Welding (AWS)
• AWS D1.1 / D1.1M - Steel
• AWS D1.2 / D1.2M - Aluminum
• AWS D1.3 / D1.3M - Sheet Steel
• AWS D1.6 / D1.6M - Stainless Steel
• AWS A2.4 - Welding Symbols
Robotics / Safety
• ISO 3691-4 - Industrial trucks safety
• ISO 13849-1 - Safety control systems
• Amazon Robotics design guidelines
Manufacturing Best Practices
• Injection molding wall and draft guides
• CNC tool reach and feature size limits
• Sheet metal bend and edge rules
• Sheet metal design guideline 930-00172_R01
• Tolerance stack-up best practices

## Slide 16
Typical Workflow
1
Upload
Drop a STEP, IGES, or STL file into the web UI or pass on the CLI.
2
Parse
Engine loads B-Rep topology, auto-detects units, extracts features.
3
Inspect
Process-specific rules run, each finding tagged with severity and location.
4
Visualize
Findings rendered on the 3D model with color-coded markers.
5
Report
Export HTML, JSON, or Word for design review or manufacturing handoff.

## Slide 17
DFM Inspector
Catch DFM violations in seconds, not weeks.
Get Started
• Launch via DFM_Inspector_Launcher.bat or python app.py
• Drop a STEP/IGES/STL file and click Analyze
• Customize thresholds in config/inspection_rules.yaml
• Hook into pipelines via JSON output